## Slide 1
Notes: Danny:
Introduce our project

## Slide 2
Advisors:
Dr. Fletcher Miller
Dr. Arlon Hunt
Daniel Cassinis
Chris Renner
May 5, 2009
Sponsor:
Google.org
Who We Are
Notes: Danny:
Read this slide, introduce us

## Slide 3
What We Are Doing
Pyrolyzing Methane Gas:
Separating carbon and hydrogen particles by addition of heat.
We are interested in the carbon.
Simplified reaction, actual reaction occurs in 4 smaller steps.
Minimum temperature for reaction is 600 °C, ideal temperature is 900 °C
Reaction time is between 0.1 to 1 second
Notes: Chris:
Describe the chemical reaction that we are performing
Mention the reaction is more complex, temperature range for reaction to occur, and residence time for reaction

## Slide 4
Why
Carbon particles have high surface area to volume
Ideal for absorbing radiant energy, transforming it to heat, and efficiently transferring the heat to a surrounding fluid
In Other Words…
The particles will absorb solar radiation, heat pressurized air until particles vaporize. Heated gas expands through a turbine ultimately generating electricity in a solar thermal power cycle.
Notes: Danny:
Discuss why we are doing this project
Briefly mention the picture; shows the configuration of current solar thermal power plants using a Rankine cycle
  The difference between the Rankine cycle and our design is the working fluid (mineral oil, liquid salts, or water vs air)
  Efficiency; approximately 15% with current technology vs experimental and theoretical efficiency of 40-45% NEED TO FIND OUT EXACT NUMBER

## Slide 5
Open Brayton Cycle Solar Thermal Power Plant
1
2
3
4
Compressor
Turbine
Carbon
Particles
Heliostats
Particle
Generator
Collector
Air
Exhaust Gases
Shaft Work Out

## Slide 6: Project Objectives
Design a particle generator that works by pyrolyzing methane gas to form carbon particles
Create a clean production of carbon particles
Control of ratio of gases and flow rates
Control of temperature
Control chamber pressure
Accurately measure particle size

## Slide 7
Reaction Chamber
CH4
N2
Note: Thermocouples and heating coil power leads not shown
Outer Chamber
Inner Chamber
Insulation
Heating Coil
Gas Injection
Head
Exit Nozzle

## Slide 8
Outer Reaction Chamber
Design Specifications
150 psi maximum pressure
200 °C maximum temperature
Flanged ends for access
ASTM A106 Grade B steel
24” length
12” inner diameter
¼ “ thickness
12 bolt 1” thick flanges

## Slide 9
Outer Reaction Chamber cont’d
Endplates extremely heavy, 120 pounds
Because we were removing them for assembly and testing, analyzed aluminum endplate (70 pound weight savings)
Static displacement of 6061 Aluminum Endplate At 150 psi
Maximum deflection of 0.00480” exceeded design specification of < 0.001”

## Slide 10
Heat Transfer Calculations
Before proceeding with design:
Heat transfer analysis was performed on system to determine:
  Insulation type and thickness required
  Ceramic tube diameter
  Power requirement for heating coil
Initial conduction analysis for 1000 °C showed insulation thickness of 3”
2-Dimiensional conduction analysis performed on system
Temperature in Kelvin. Credit: Steve Ruther
Results:
3” insulation thickness acceptable starting point
1” inner diameter tube preferred
650 W minimum power requirement
Surface temperature of steel chamber < 100 °C

## Slide 11
Porous Ceramic Inner Chamber
Built flow tunnel to test pressure drop across ceramic samples
65 pores per linear inch, 92% Al2O3 alumina chosen
Diameter determined by previous heat transfer calculations
24” long
1” inner diameter
¼” thickness

## Slide 12
Insulation
Durablanket S chosen because of flow testing and heat transfer calculation results
  ¼” thickness
  6.0 lb/ft^3 density
Thickness in reaction chamber controlled by layering
Material also has exceptional durability and bending radius

## Slide 13
Heating System
Heating Coil
Kanthal “A-F” wire coil
1200 Watts @ 120 Volts
Control and Displays
Honeywell UDC 2500 Universal Digital Controller
  Tunable PID and custom user defined temperature profiles
  Precision Digital Temperature Indicators
  Type K inconel sheath thermocouples
Temperature Displays
Controller
Thermocouples

## Slide 14
Heating System
Purchased components, wired and programmed ourselves to save money
Temperature Displays
20 Amp Relay
Digital Controller
Thermocouples
Heating Coil
Power Feedthroughs

## Slide 15
Gas System
Gases used are nitrogen and methane
3 Alicat mass flow controllers are used to control gas flow rates and ratios;
  1 for methane
  2 for nitrogen; injection head and chamber fitting
  2 Airgas pressure regulators used to control gas pressure
Mass Flow Controllers
Pressure Regulator

## Slide 16
Gas System Cont’d
Gas Injection Head
Coaxial gas flow of nitrogen and methane to prevent coking at methane injection point
Allows depth of gas injection to be controlled for both gases
N2 Line
CH4 Line
CH4
N2
N2
Outlet Valve
Risk of explosion or fire at chamber exit; high temperatures, O2, and H2
Designed nozzle to fit in exit
  Controls pressure drop and prevents backflow
1” NPT fitting
Nozzle

## Slide 17
Results
Assembly and setup of all key components complete
Bench testing of all reaction chamber subsystems complete:
  Gas pressure and flow control functional
  Digital controller programmed and coil powered, temperature control functional
  Thermocouples tested and functional
  Inner tube, chamber endplate interface verified
  All major safety concerns have been addressed
Final task is to perform test runs and generate first batch of carbon, concluding first year of the project
Design Specifications:
Carbon Particle Density: 1 – 3 g/m3
Residence Time: ≤ 1 sec

## Slide 18
Acknowledgements
Dr. Fletcher Miller
Dr. Arlon Hunt
Google.org
Industronics
Hi Tech Ceramics
Swagelok
San Diego Electronic Supply
Omega
PAVE
Tidelands Oil
McMaster Carr and Marshall’s Hardware

## Slide 19
Questions?